## Slide 1: Path to Production Data: SeaQuest Spectrometer
EMG Meeting
Paul E Reimer
13 December 2013

## Slide 2: Commissioning—Hodoscopes
Verify
  Channel Mapping ✔
  Gain Match ✔
  Test New Base Design--Illinois ✔
  Does not appear to sag at high rate
  Better gain (removed amplifiers)
  Verify Timing ✔

## Slide 3: Commissioning—Tracking Chambers
Verify
  Channel Mapping ✔
  Plateau studies
    In progress/finished early next week
  R(t) curves

## Slide 4: Present tasks
Trigger Commissioning
  Do all triggered events contain roads on which we should trigger
  Do “NIM” triggered events with roads contain an FPGA signal
The trigger is not a “black box”—its more like a Red box with grey cables all over
Spectrometer Alignment with Tracking
Beam Cherenkov
  Quantify Luminosity blocked and delivered
  Full spill readout
  Quantify how much needs to be blocked and still track events

## Slide 5: On Going Issues—St. 1
St. 1 X Tracking Chamber
  Plane MIA
  Will investigate on Tuesday/Wednesday Access

## Slide 6: On Going Issues—St. 2
St. 2U Tracking Chamber
  Large current draw.
  Operating at reduced voltage.
  Approx. 25% efficiency
  Believe this is a broken wire.
  Will investigate on Tuesday/Wednesday Access

## Slide 7: On Going Issues—Hall Radiation
Radiation levels appear to be higher than scaling from commissioning run
Possibly from newly installed beam Cherenkov
Solutions:
  Move Cherenkov to NM2
  Move Cherenkov nearer to target cave
  Additional shielding
Vacuum
Windows
Beam
Mylar Mirror
Cherenkov

## Slide 8: Other Items
New St. 1 Chamber
Ongoing work at Colorado
Wire stringing should be completed before Holiday break
Gas enclosure completed in early February
Assembly, testing and replacement of some wires in Lab 6 late February
Grid Computing
Started to use grid for MC and plan to move analysis there
Very light load
Sewer
FESS may need to dig near/under our beam line to resolve an issue with the sewer line from IARC and Feynman.
Presently this is thought to be a week of downtime, but not yet scheduled

## Slide 9: Commissioning Summary
Targets ready and waiting
Magnets ready and waiting
Hodoscopes ready and waiting
Tracking
  2 planes need repair—Tuesday and Wednesday
  most voltage plateau curves complete
  22/24 planes ready and waiting
  Prop. Tubes ready and waiting
Trigger testing in progress
  (This weekend)
Beam Cherenkov/splat block code work
Open questions
  Beam quality (Don’s Talk)
  Sewer Repair?
Ready to go soon!